Operation Permit Inspection Checklist

| The following items are on file and part of this permitting process: |
| --- |
|  | ( | GPS/GIS | ( | IP/CA | ( | Map | ( | Engineer’s Plans & Specs |
|  | ( | Application | ( | Soil Sheet | ( | Plat Map | ( | O & M Manual |
| 1. | LOCATIONS AND SEPARATION DISTANCES |  | Satisfactory | N/A | Problem |
|  | System meets Rule .1950 setback requirements |  | ( | ( | ( |
|  | Distance from system to any wells |  | ( | ( | ( |
|  | Distance from septic tank to foundation |  | ( | ( | ( |
|  | Distance from system to all property lines |  | ( | ( | ( |
| 2. | BUILDING SANITARY SEWER |  | Satisfactory | N/A | Problem |
|  | Wastewater pipes connected to system per approved plans |  | ( | ( | ( |
|  | Wastewater piping materials and ratings meet Rule .1955 |  | ( | ( | ( |
|  | Cleanouts provided and located per approved plans |  | ( | ( | ( |
|  | Backfill material clean |  | ( | ( | ( |
| 3. | SEPTIC TANKS |  |  |  |  |
|  |  | Tank #1 | Tank #2 | Tank #3 | Tank #4 |
|  | Tank serial number (i.e., PT-XXXX per manufacturer imprint) |  |  |  |  |
|  | Tank manufacture date (per manufacturer imprint) |  |  |  |  |
|  | Approved tank liquid capacity, gallons (per manufacturer’s imprint) |  |  |  |  |
|  | Gallons per inch, gpi (based on approved tank liquid capacity) |  |  |  |  |
|  | Concrete compressive strength, psi (per manufacturer) |  |  |  |  |
|  | Leak test date |  | Test start time |  | Test end time |  |  |
|  | Static Test |  | Vacuum Test (Minimum Hold Time = 2 mins) |
|  | Starting water level |  | inches |  | Starting negative pressure |  | inches of Hg |
|  | Ending water level |  | inches |  | Ending negative pressure |  | inches of Hg |
|  | Water level difference |  | inches |  | Negative pressure difference |  | inches of Hg |
|  | 1% of tank liquid capacity |  | inches |  | 10% of starting negative pressure |  |  |
|  | Difference < 0.5” or 1% of tank capacity | ( Yes ( No | Difference < 10% of starting pressure | ( Yes ( No |  |

|  | SEPTIC TANKS (continued) |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Septic Tank Conditions |  | Satisfactory | N/A | Problem |
|  | Tanks are required size/loading per approved plans and specifications |  | ( | ( | ( |
|  | Condition of the exterior walls and top of the tanks |  | ( | ( | ( |
|  | Air vents present and open |  | ( | ( | ( |
|  | Condition of risers and access lids |  | ( | ( | ( |
|  | Condition of the interior walls (inlet, outlet, baffle, and bottom) |  | ( | ( | ( |
|  | Tanks are watertight (no evidence of infiltration) |  | ( | ( | ( |
|  | Inlets and outlets are at proper location |  | ( | ( | ( |
|  | Inlet and outlet tees on center line |  | ( | ( | ( |
|  | Approved filter devices placed at outlets |  | ( | ( | ( |
|  | Inlet elevation |  | feet |  |  |
|  | Outlet elevation |  | feet | (must be 2” lower than inlet w/ 9” freeboard present) |  |
| 4. | SYSTEM TYPE |  |
|  | Distribution Type | ( | Gravity | ( | Pump | ( | Siphon |  |
|  | Controls Type | ( | Control Panel | ( | Piggyback |  |  |  |
| 5. | PUMP TANKS |  |  |  |  |
|  |  | Tank #1 | Tank #2 | Tank #3 | Tank #4 |
|  | Tank serial number (i.e., PT-XXXX per manufacturer imprint) |  |  |  |  |
|  | Tank manufacture date (per manufacturer imprint) |  |  |  |  |
|  | Approved tank liquid capacity, gallons (per manufacturer’s imprint) |  |  |  |  |
|  | Gallons per inch, gpi (based on approved tank liquid capacity) |  |  |  |  |
|  | Concrete compressive strength, psi (per manufacturer) |  |  |  |  |
|  | Design pump rates, gallons per minute (gpm) |  |  |  |  |
|  | Leak test date |  | Test start time |  | Test end time |  |  |
|  | Static Test |  | Vacuum Test (Minimum Hold Time = 2 mins) |
|  | Starting water level |  | inches |  | Starting negative pressure |  | inches of Hg |
|  | Ending water level |  | inches |  | Ending negative pressure |  | inches of Hg |
|  | Water level difference |  | inches |  | Negative pressure difference |  | inches of Hg |
|  | 1% of tank liquid capacity |  | inches |  | 10% of starting negative pressure |  |  |
|  | Difference < 0.5” or 1% of tank capacity | ( Yes ( No | Difference < 10% of starting pressure | ( Yes ( No |  |

|  | PUMP TANKS (continued) |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Pump Tank Conditions |  | Satisfactory | N/A | Problem |
|  | Tank is required size/loading per plan |  | ( | ( | ( |
|  | Condition of the exterior walls and top of the tank |  | ( | ( | ( |
|  | Air vent present and open |  | ( | ( | ( |
|  | Condition of risers and access lids |  | ( | ( | ( |
|  | Pump access is lockable or secured to prevent unauthorized entry |  | ( | ( | ( |
|  | Pump access riser extends to at least 6” above finished grade |  | ( | ( | ( |
|  | Condition of the interior walls (inlet, outlet, baffle, and bottom) |  | ( | ( | ( |
|  | Inlet and outlet are at proper location |  | ( | ( | ( |
|  | Pump assembly is reachable from the surface without tank entry |  |  |  |  |
|  | Pump removal rope, chain, or lifting device |  | ( | ( | ( |
|  | Independent float support system |  | ( | ( | ( |
|  | Valves (check and shut-off) and vent installed /properly functioning |  | ( | ( | ( |
|  | Pump disconnects (unions) are accessible without tank entry |  | ( | ( | ( |
|  | Bollards or other protective devices |  | ( | ( | ( |
| 6. | SIPHONS |  |  |  |  |
|  |  |  | Satisfactory | N/A | Problem |
|  | Siphons are operable |  | ( | ( | ( |
|  | Siphons are installed under access opening |  | ( | ( | ( |
|  | Siphons are removable from the surface without tank entry |  | ( | ( | ( |
|  | Siphon cycle counters are operable |  | ( | ( | ( |
|  | Siphon access is lockable or secured to prevent unauthorized entry |  | ( | ( | ( |
| 7. | CONTROL PANELS |  |  |  |  |
|  |  | Panel #1 |  | Panel #2 |
|  | Manufacturer |  |  |  |
|  | Model Number |  |  |  |
|  | Location |  |  |  |
|  |  | Panel #3 |  | Panel #4 |
|  | Manufacturer |  |  |  |
|  | Model Number |  |  |  |
|  | Location |  |  |  |

|  | CONTROL PANELS (continued) |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Control Panel Conditions |  | Satisfactory | N/A | Problem |
|  | Enclosure watertight |  | ( | ( | ( |
|  | NEMA 4X rated enclosure |  | ( | ( | ( |
|  | Installed a minimum of 12” above finished grade |  | ( | ( | ( |
|  | HAND-OFF-AUTO (H-O-A) switch operable |  | ( | ( | ( |
|  | Pump and alarm on separate circuits |  | ( | ( | ( |
|  | Water/gas/corrosion-proof conduit |  | ( | ( | ( |
|  | No internal splices |  | ( | ( | ( |
|  | Alarm (visual and audible) functioning properly |  | ( | ( | ( |
|  | Manual disconnect present and accessible |  | ( | ( | ( |
|  | Electrical inspection conducted |  | ( | ( | ( |
|  | Timer operable |  | ( | ( | ( |
|  | Elapsed time meter operable |  | ( | ( | ( |
|  | Cycle counter operable |  | ( | ( | ( |
|  | Telemetry operable |  | ( | ( | ( |
|  | Control Panel - Dispersal Field Pump/Dosing Tank |  |
|  | H-O-A switch set at: | ( | Auto |  | ( | Hand/Manual |  | ( | Off |  |
|  | Why: |  |  |
|  | Timer Setting: | On Mode setting |  | minutes |  |
|  |  | Off Mode setting |  | ( | minutes | ( | hours |  |
|  | Elapsed Time Meter Reading: |  | ( N/A |  |
|  | Cycle Counter Reading: |  | ( N/A |  |
| 8. | PUMPS |  |  |
|  | Electrical Considerations |  | Satisfactory | N/A | Problem |
|  | Power supply available |  | ( | ( | ( |
|  | Amps measured [_____________ amps] |  | ( | ( | ( |
|  | Voltage measured [_____________ volts] |  | ( | ( | ( |
|  | Electrical service | ( | Single-phase 120V | ( | Single-phase 240V |  |  |  |
|  |  | ( | 3-phase 240/120V | ( | 3-phase 208/120V |  |  |  |
|  | Tank & Pump # |  |  |  |  |  |  |
|  | Manufacturer(s) |  |  |  |  |  |  |
|  | Model(s) |  |  |  |  |  |  |
|  | Type of pump* |  |  |  |  |  |  |
|  |  | * For example, multi-stage, single-stage, sewage, effluent, or grinder. |  |
|  | Design flow rate |  | gpm |  | gpm |  | gpm |
|  | Design TDH |  | feet |  | feet |  | feet |
|  | Horsepower |  | hp |  | hp |  | hp |

|  | PUMPS (continued-1) |  |
| --- | --- | --- |
|  | Tank & Pump # |  |  |  |  |  |  |
|  | Manufacturer(s) |  |  |  |  |  |  |
|  | Model(s) |  |  |  |  |  |  |
|  | Type of pump* |  |  |  |  |  |  |
|  |  | * For example, multi-stage, single-stage, sewage, effluent, or grinder. |  |
|  | Design flow rate |  | gpm |  | gpm |  | gpm |
|  | Design TDH |  | feet |  | feet |  | feet |
|  | Horsepower |  | hp |  | hp |  | hp |
|  | Pump Conditions |  | Satisfactory | N/A | Problem |
|  | Pumps are operable |  | ( | ( | ( |
|  | Pump access is a minimum of 6” above finished grade |  | ( | ( | ( |
|  | Pump assembly is reachable from the surface without tank entry |  | ( | ( | ( |
|  | Quick disconnects are operable |  | ( | ( | ( |
|  | Isolation valves are operable |  | ( | ( | ( |
|  | Anti-siphon/air release devices are operable |  | ( | ( | ( |
|  | Backflow prevention (check valves) are operable |  | ( | ( | ( |
|  | Air releases located below check valves are operable |  | ( | ( | ( |
|  | Drainback devices are operable |  | ( | ( | ( |
|  | Inline filters are operable |  | ( | ( | ( |
|  | Pressure gauges/ports are operable |  | ( | ( | ( |
|  | Sampling ports are operable |  | ( | ( | ( |
|  | Pump removal system installed/in place |  | ( | ( | ( |
|  | ( | Stainless steel pull-chain | ( | Pull rope | ( | Pump rails |  |  |
|  | ( | Other |  |  |
|  | Water Level Sensors |  |  |  |  |
|  | Type of water level sensor | ( | Floats | ( | Pressure transducers |  |  |
|  |  | ( | Ohm probe | ( | Other |  |  |
|  | Sensor attachment | ( | Tethered to float trees | ( | Weighted tethers from risers |  |
|  |  | ( | Attached to float brackets/racks | ( | Attached to risers |  |
|  | Water Level Sensor Conditions | Satisfactory | N/A | Problem |  |
|  | Float trees/assemblies are removable | ( | ( | ( |  |
|  | Alarm floats/sensors operate audible alarm | ( | ( | ( |  |
|  | Alarm floats/sensors operate visible alarm | ( | ( | ( |  |
|  | Pumps are submerged at OFF elevations/levels | ( | ( | ( |  |

|  | PUMPS (continued-2) |  |
| --- | --- | --- |
|  | Dosing Design Parameters |  |  |  |  |
|  |  | Tank & Pump # | Demand Dosing | Timed Dosing |  | Dosing Volume |  |
|  |  |  | ( | ( |  |  | gals |
|  |  |  | ( | ( |  |  | gals |
|  |  |  | ( | ( |  |  | gals |
|  |  |  | ( | ( |  |  | gals |
|  |  |  | ( | ( |  |  | gals |
|  |  |  | ( | ( |  |  | gals |
|  | Pump Rate Measurements |  |  |  |  |
|  | Ending Depth – Beginning Depth = Drawdown, inches Drawdown, inches X Tank gpi = Drawdown, gallons Drawdown, gallons ÷ Pump Run, minutes = Pump, gpm |  |
|  | Pump # | Beginning Depth | Ending Depth | Drawdown, inches | Tank gpi | Drawdown, gallons | Pump Run, minutes | Pump, gpm |
| 9. | SUPPLY LINES TO DISPERSAL AREAS |  |  |  |  |
|  |  | Line #1 | Line #2 | Line #3 | Line #4 |  |
|  | Grade, foot/foot (1/8 inch per foot minimum) |  |  |  |  |  |
|  | Material (e.g., Schedule 40 PVC, ductile iron, etc.) |  |  |  |  |  |
|  | Diameter, inches |  |  |  |  |  |
|  | Length, feet |  |  |  |  |  |
|  | Distance from tank to dispersal area/distribution device |  |  |  |  |  |
|  | Pressure head at discharge point, feet |  |  |  |  |  |
| 10. | DISPERSAL METHOD |  |  |  |  |
|  | Dispersal Type |  | ( | Gravity | ( | LPP | ( | Drip |
|  |  |  | ( | Other (please specify) |  |

| 11. | DISTRIBUTION DEVICES |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Number of distribution devices |  |  |  |  |
|  |  | Device #1 | Device #2 | Device #3 | Device #4 |  |
|  | Type (e.g., d-box, pressure manifold, other) |  |  |  |  |  |
|  | Number of outlets/laterals per distribution device |  |  |  |  |  |
|  | Device serves which dispersal areas? |  |  |  |  |  |
|  | Distribution Device Conditions | Satisfactory | N/A | Problem |  |
|  | Distribution devices are watertight | ( | ( | ( |  |
|  | Minimum of 2 feet undisturbed soil to trench | ( | ( | ( |  |
|  | Proper center to center trench spacing maintained | ( | ( | ( |  |
|  | Devices installed on solid foundations | ( | ( | ( |  |
|  | All outlet inverts properly adjusted | ( | ( | ( |  |
|  | Turnups/cleanouts/valves are accessible | ( | ( | ( |  |
|  | Devices perform according to design specifications | ( | ( | ( |  |
|  | Lateral Elevations |  |  |  |  |
|  |  | Device #1 | Device #2 | Device #3 | Device #4 |
|  | Lateral # | Lateral Length, feet | Inlet | Outlet | Inlet | Outlet | Inlet | Outlet | Inlet | Outlet |
|  | 1 |  |  |  |  |  |  |  |  |  |
|  | 2 |  |  |  |  |  |  |  |  |  |
|  | 3 |  |  |  |  |  |  |  |  |  |
|  | 4 |  |  |  |  |  |  |  |  |  |
|  | 5 |  |  |  |  |  |  |  |  |  |
|  | 6 |  |  |  |  |  |  |  |  |  |
|  | 7 |  |  |  |  |  |  |  |  |  |
|  | 8 |  |  |  |  |  |  |  |  |  |
|  | 9 |  |  |  |  |  |  |  |  |  |
|  | 10 |  |  |  |  |  |  |  |  |  |
| 12. | DISPERSAL AREAS/FIELDS |  |  |  |  |
|  | Trench depth |  | feet | Trench width |  | feet | Trench spacing |  | feet |
|  | Aggregate depth |  | inches |  |  |  |  |  |  |
|  | Aggregate material |  | ( | Rock | ( | Polystyrene | ( | Tire chip |
|  |  |  | ( | Other (please specify) |  |

|  | DISPERSAL AREAS/FIELDS (continued) |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Trench Product |  |  |  |  |
|  | Manufacturer name |  |  |
|  | Product name and model |  |  |
|  | Trench Conditions |  | Satisfactory | N/A | Problem |
|  | Installation depth per approved plans and specifications |  | ( | ( | ( |
|  | Soil cover adequate and per approved plans and specifications |  | ( | ( | ( |
|  | Trench spacing per approved plans and specifications |  | ( | ( | ( |
|  | Proper effluent distribution |  | ( | ( | ( |
|  | Pressure head meets parameters in approved specifications |  | ( | ( | ( |
|  | Product installation meets manufacturers specifications |  | ( | ( | ( |
|  | Stepdown Conditions |  | Satisfactory | N/A | Problem |
|  | Constructed of minimum 2 linear feet of undisturbed soil |  | ( | ( | ( |
|  | Proper rise over stepdowns |  | ( | ( | ( |
|  | Constructed height fully utilizes the upstream trench |  | ( | ( | ( |
|  | Backfilled with compacted soil |  | ( | ( | ( |
|  | Solid (non-perforated) pipe used between stepdowns |  | ( | ( | ( |
|  | Supply pipe inlet invert 1” above supply pipe outlet invert |  | ( | ( | ( |
|  | Top of trench outlet 2” below supply pipe outlet invert |  | ( | ( | ( |
|  | Stepdown # |  | Elevation |  | Dispersal Field ID |  | Connected Lateral # |  |
|  |  |  |  | feet |  |  |  |  |
|  |  |  |  | feet |  |  |  |  |
|  |  |  |  | feet |  |  |  |  |
|  |  |  |  | feet |  |  |  |  |
|  |  |  |  | feet |  |  |  |  |
|  |  |  |  | feet |  |  |  |  |
|  |  |  |  | feet |  |  |  |  |
|  |  |  |  | feet |  |  |  |  |
|  |  |  |  | feet |  |  |  |  |
|  |  |  |  | feet |  |  |  |  |

| 14. | ADVANCED PRE-TREATMENT |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Manufacturer name |  |  |
|  | Product name and model |  |  |
|  | NOTE: Refer to the advanced pre-treatment product approval and manufacturer’s product manuals for specific installation and O&M requirements |
|  | Advanced Pretreatment Conditions |  | Satisfactory | N/A | Problem |
|  | Units installed per manufacturer specifications and approved plans |  | ( | ( | ( |
|  | Signed copy of installation certification received from system designer |  | ( | ( | ( |
|  | System ORC is present at the site |  | ( | ( | ( |
|  | O & M procedures have been provided |  | ( | ( | ( |
|  | Sampling and monitoring requirements are in place |  | ( | ( | ( |
|  | Sample collections locations identified |  | ( | ( | ( |
|  | System operation checks performed |  | ( | ( | ( |
| 15. | ADDITIONAL COMMENTS: |  |  |  |  |

See “as-built” plan on attached sheet